## Slide 1: One Bit Flips, One Cloud Flops: Cross-VM Row Hammer Attacks and Privilege Escalation
Yuan Xiao, Xiaokuan Zhang, Yinqian Zhang, Radu Teodorescu
The Ohio State University
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
Row Hammer

## Slide 2: Row Hammer Vulnerabilities and Exploits
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
Once thought safe, DDR4 memory shown to be vulnerable to “Rowhammer”, March 17 2016
Row Hammer DRAM Bug Now Exploitable via JavaScript, Most DDR3 Memory Chips Vulnerable, July 29 2015
Flipping DRAM bits - maliciously, December 29, 2014
Row Hammer DRAM Bug Exploited, Unlocks Access to Physical Memory, March 9 2015

## Slide 3: DRAM Architecture
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
Data bus
64-bit
Channel
DIMM
Rank 0 (front)
Rank 1 (back)

## Slide 4: Row Buffer and Row Activation
Bank
Columns
Rows
Row Buffer
Activation (Charging)
I/O Bus
Read/Write
A memory block (one byte)
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 5: Disturbance Errors (1)
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
rapid row activation
[ISCA‘14] Kim et al.
Row Buffer
one bit,
not one byte.
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 6: Disturbance Errors (2)
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
bit flips in neighboring rows
rapid row activation
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
[ISCA‘14] Kim et al.
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
Row Buffer

## Slide 7: Double-sided Row Hammer Attack
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
Hammering Rows
(Upper)
Victim Row
(Middle)
High-risk Victim Row
(Lower)
Victim Row
Row Buffer
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 8: Related Work
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
Kim, et al. [ISCA ‘14]
Seaborn (Google), 2015
R3dF09 (Tencent), 2015
Bosman, et al. [SOSP ‘16]
Gruss, et al. [DIMVA ’16]
Single-sided vs. double-sided row hammer
Exploitation scenarios

## Slide 9
How to conduct double-sided row hammer attacks?
How to exploit row hammer vulnerabilities in cross-VM settings?
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 10: Outline
Reverse-engineer DRAM Mapping
Cross-VM Row Hammer Exploitation
Case studies
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 11: Difficulties in Double-sided Row Hammer
Physical Address
x2
Physical Address
x1
Which bank?
Which row?
Which bank?
Which row?
Same bank?
Neighboring rows?
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 12: A Basic Timing Channel Primitive
Row Buffer
 |  | x1 |  | 
Column
Row
Row Buffer
 | x2 |  |  | 
Column
Row
Bank b1
Bank b2
 |  | x1 |  | 
 | x2 |  |  | 
Row Buffer
Row Buffer
read x1
read x2
T1=2*Tactivate
+2*n*Tread
Tactivate
Tread
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 13: Basic timing channel primitive
 |  | x1 |  | 
 | x2 |  |  | 
Row Buffer
Column
Row
Bank
 |  | x1 |  | 
 | x2 |  |  | 
Row Buffer
Row Buffer
read x1
read x2
T2=2*n*Tactivate
+2*n*Tread
T1=2*Tactivate
+2*n*Tread
T2-T1=2*(n-1)*Tactivate
T2 > T1
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 14: Basic timing channel primitive
High latency
same bank
different row
What if the two physical addresses differ only in specific bit positions?
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 15: Row Bit Detection
… | 21 | 20 | 19 | 18 | 17 | …
… | 0 | 0 | 1 | 0 | 0 | …
… | 0 | 1 | 1 | 0 | 0 | …
Physical Address x1
Bit Index of a Physical Address
Physical Address x2
High latency?
Bit 20 decides the row, but not the bank.
 | 21 | 20 | 19 | 18 | 17 | 
 | 21 | 20 | 19 | 18 | 17 | 
Read
Read
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 16: Column Bit Detection
… | 21 | 20 | … | 4 | 3 | …
… | 0 | 0 | … | 0 | 0 | …
… | 0 | 1 | … | 1 | 0 | …
Physical Address y1
Bit Index of a Physical Address
Physical Address y2
High latency?
Bit 20 decides the row, but not the bank.
 | 21 | 20 | … | 4 | 3 | 
 | 21 | 20 | … | 4 | 3 | 
Read
Read
Bit 4 does not decide
the bank.
(but decides column)
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 17: Row/Column Bit Summary
Bit Index of a Physical Address
row bits
column bits
other bits
White bits: always show low latency in previous two kinds of tests.
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 18: XOR Scheme Detection (1)
… | 19 | 18 | 17 | 16 | 15 | …
Row Bit
Bank Bit
+
… | 0 | 0 | 1 | 0 | 0 | …
… | 0 | 1 | 1 | 1 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
 | 19 | 18 | 17 | 16 | 15 | 
Physical Address z1
Physical Address z2
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 19: XOR Scheme Detection (2)
… | 0 | 0 | 1 | 0 | 0 | …
… | 0 | 1 | 1 | 1 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
 | 19 | 18 | 17 | 16 | 15 | 
Read
Read
High latency?
Physical Address z1
Physical Address z2
different row
same bank
Either 18 or 16 decides the row
Bit 18 (higher bit) should be row bit
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 20: XOR Scheme Detection (3)
test | 18 | 16 | 18 ⊕ 16 | latency | bank | row
1 | 1 0 | 1 1 | 0 1 | low | different | different
2 | 1 0 | 1 0 | 0 0 | high | same | different
3 | 1 0 | 0 1 | 1 1 | high | same | different
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 21: XOR Scheme Detection (4)
18 ⊕ 16 | bank
0 1 | different
0 0 | same
1 1 | same
… | 19 | 18 | 17 | 16 | 15 | …
Row Bit
Bank Bit
+
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 22: Graph-based Bit Detection Algorithm
18
14
13
… | 19 | 18 | 17 | 16 | 15 | 14 | 13 | …
Row Bit
Bank Bit
+
16
+
+
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 23: Graph-based Bit Detection Algorithm
18
15
16
20
… | 21 | 20 | 19 | 18 | 17 | 16 | 15 | …
Row Bit
Bank Bit
+
+
+
Row Bit
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 24: Graph-based Bit Detection Algorithm
18
15
16
20
… | 21 | 20 | 19 | 18 | 17 | 16 | 15 | …
Row Bit
Bank Bit
+
+
+
Row Bit
17
+
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 25: Outline
Reverse-engineer DRAM Mapping
Cross-VM Row Hammer Exploitation
Case studies
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 26: Virtualization and Cloud Computing
Hardware
Hypervisor
Virtual Machines
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 27: Xen Para-Virtualized instances in Real-world Public Clouds
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 28: Xen Para-Virtualized Memory Management
CR3
Virtual Address (Application)
Pseudo Physical Address (Kernel)
Machine Address (Hypervisor)
PGD
PUD
PMD
PT
Page
All the page tables are maintained in the guest kernel
Pointing to machine addresses
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 29: Page Table Management
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
Virtual address
PGD
CR3
pgd_t
PUD
pud_t
PMD
pmd_t
PT
pte_t
Page
All the page tables are read-only to the guest kernel
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 30: Xen PV memory management
Hypervisor
Target physical address belonging to VM 1?
Guest VM 1
Guest VM 2
…
Hypercall
No
Yes
CR3
PGD
PUD
PMD
PT
Page
1
Page
2
Change of entry?
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 31: Page Table Replacement Attack (1)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
PMD
pmd_t
PT
pte_t
Original state
Attacker-controlled Page
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 32: Page Table Replacement Attack (2)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
PMD
pmd_t
PT
pte_t
Forged PT
malicious pte_t
Malicious PT forged
Attacker-controlled Page
Arbitrary Page
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 33: Page Table Replacement Attack (2)
Forged PT
… | 0 | 0 | 1 | 0 | 0 | …
… | 0 | 1 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
 | 19 | 18 | 17 | 16 | 15 | 
PT
The addresses of PT and Forged PT only differ in one particular bit.
Machine address of PT
Machine address of Forged PT
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 34: Page Table Replacement Attack (2)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
PMD
pmd_t
PT
pte_t
Forged PT
malicious pte_t
Malicious PT forged
Attacker-controlled Page
Arbitrary Page
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 35: Page Table Replacement Attack (3)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
Vulnerable
Page
pmd_t
PT
pte_t
Attacker-controlled Page
Forged PT
pte_t’
Arbitrary Page
vulnerable pmd_t
PMD
pmd_t
PMD copied to vulnerable page
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 36: Page Table Replacement Attack (3)
… | 0 | 0 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
PT
… | 0 | 0 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
Machine address of PT
pmd_t
(Shadow) PMD
pmd_t
vulnerable bit
… | 0 | 1 | 1 | 0 | 0 | …
Machine address of Forged PT
 | 19 | 18 | 17 | 16 | 15 | 
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 37: Page Table Replacement Attack (3)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
Shadow
PMD
pmd_t
PT
pte_t
Attacker-controlled Page
Forged PT
pte_t’
Arbitrary Page
vulnerable pmd_t
PMD
pmd_t
PMD copied to vulnerable page
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 38: Page Table Replacement Attack (4)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
Shadow
PMD
pmd_t
PT
pte_t
Forged PT
pte_t’
Arbitrary Page
Shadow PMD enabled via hypercall
Attacker-controlled Page
… | 0 | 0 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 39: Page Table Replacement Attack (4)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
Shadow
PMD
pmd_t
PT
pte_t
Forged PT
pte_t’
Arbitrary Page
Attacker-controlled Page
… | 0 | 0 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
Shadow PMD enabled via hypercall
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 40: Page Table Replacement Attack (5)
PGD offset | PUD offset | PMD offset | PTE offset | Page offset
PGD
CR3
pgd_t
PUD
pud_t
Shadow
PMD
pmd_t’
Forged PT
pte_t’
Bit flipped by row hammer
Arbitrary Page
… | 0 | 1 | 1 | 0 | 0 | …
 | 19 | 18 | 17 | 16 | 15 | 
writable
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 41: Outline
Reverse-engineer DRAM Mapping
Cross-VM Row Hammer Exploitation
Case studies
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 42: OpenSSH Server Authentication Bypass
Attacker VM
OpenSSH Server VM
Hypervisor
Physical Machine
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 43: OpenSSH Server: Attack Target
callq pam_authenticate
test %eax, %eax jne <error handling>
mov $0, %eax
test %eax, %eax jne <error handling>
Machine code: E8 1B 74 FD FF
Machine code: B8 00 00 00 00
Primary goal: code modification
eax equals to 0?
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 44: OpenSSH Authentication Bypass (2)
Attacker VM
OpenSSH Server VM
Physical Machine
page table replacement
arbitrary memory access
search for pattern
“E8 1B 74 FD FF”
(callq pam_authenticate)
change into
“B8 00 00 00 00”
(mov $0 %eax)
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu
In the first page: 0.3 s
Per extra page: 58 μs

## Slide 45: OpenSSH Authentication Bypass (3)
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 46: Existing Countermeasures
ECC (Error Correcting Code)
DDR4 (TRR - Target Row Refresh)
HVM (Hardware-assisted Virtualization)
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu

## Slide 47: Conclusion
We use timing channel to reverse-engineer the physical address mapping to the DRAM.
We conduct efficient double-sided row hammer attacks.
Xen PV can be exploited by row hammer and allow cross-VM access.
Y. Xiao, X. Zhang, Y. Zhang, R. Teodorescu